## Slide 1: Case Study: Therac-25 Software & Safety Failure Case Study

## Slide 2: Group Members
400622038914 - TIFFANY AFRAKUMA ANKUMA PLANGE
400622039070 – MICHAEL OFOSU KORANTENG
400622038925 – TILONLEEB KONLAN
400622039195 – AARON KWESI FYNN

## Slide 3
Background & machine context
Plain-language summary of the overdoses
Timeline & example incident trace
Technical root causes
Formal verification approaches
Practical mitigations & checklist
Conclusion & references

## Slide 4: Abstract
Therac-25 function: a computer-controlled linear accelerator for cancer therapy
Design choice: replaced many hardware interlocks with software control
Operator workflow: console data entry and mode selection

## Slide 5: Introduction
Several patients received massive radiation overdoses in the mid-1980s; some resulted in severe injury and death.
Simple explanation: a particular rapid sequence of operator inputs and timing could make the machine switch modes incorrectly, and because hardware protections were absent, dangerous radiation was delivered.

## Slide 6: Detailed incident timeline
Operator inputs parameters → input handler updates shared state
Beam controller reads state during a timing window → mode transition incomplete
Beam enabled without target → overdose delivered → cryptic error shown

## Slide 7: Technical root causes
Race condition / concurrency bug in control software (unsynchronized access to shared variables)
Overreliance on software for safety hardware interlocks removed or weakened
Poor error reporting and a failure to model realistic fast operator behavior.

## Slide 8: Evidence & example reproductions
Reconstructed keystroke interleaving trace that the model checker would output as a counterexample
Mock console logs showing cryptic error messages and timing marks

## Slide 9: How formal methods would have helped
Model checking of the composed user + machine model to exhaustively find unsafe interleavings
Formal temporal properties such as `Beam_ON → TargetInPlace`
Runtime assertions (in code) as a last line of defense plus independent hardware watchdogs

## Slide 10: Practical mitigations & checklist (detailed)
Reintroduce independent hardware interlocks for critical physical functions
Use model-based tests and model checking that include realistic operator models
Improve error reporting to provide actionable diagnostics and add robust logging for post-incident analysis

## Slide 11: System-Level Integration
Failures often arise from interactions, not single components.
Formal integration models all components (IRUs, OBC, actuators) together.
Verification ensures redundancy and diagnostics behave correctly under fault conditions.

## Slide 12: References & further reading
Clarke, E. M., Grumberg, O., & Peled, D. (1999). Model Checking. MIT Press.
De Moura, L., & Bjørner, N. (2008). Z3: An Efficient SMT Solver. In Tools and Algorithms for the Construction and Analysis of Systems.
King, J. C. (1976). Symbolic Execution and Program Testing. Communications of the ACM.
Leveson, N. G. (1995). Safeware: System Safety and Computers. Addison-Wesley.
Leveson, N. G., & Turner, C. S. (1993). An Investigation of the Therac-25 Accidents. IEEE Computer.
Meyer, B. (1992). Applying "Design by Contract". IEEE Computer.
Notes: Detailed speaker note:
The narrative and technical traces presented here are drawn from the uploaded Therac-25 case study and seminal analyses (Leveson & Turner, 1993). For deeper methods and concrete model-checker examples, see the references in the appendix. The uploaded document includes suggested temporal properties and illustrative model-checking approaches used to find the concurrency counterexample.
Plain-language explanation:
If you want more reading, the references include accessible summaries of the incidents and practical papers about safety in medical devices.